## Slide 1: Computer Organisation
Topic 1
Introduction
(Part 1)
Stallings, Computer Organization & Architecture (9th Ed.), Chap. 1

## Slide 2: Outline
Organisation and architecture
Structure and function
Computer evolution and performance
Cloud Computing
Performance Issues
  History of computers
  X86, PowerPC and ARM evolution

## Slide 3: Architecture & Organisation
Architecture is those attributes visible to the programmer (programmer’s view of a computer)
It is defined by the instruction set
(language), and operand locations (registers and memory).
  Deals with the functional behaviour of a computer system
  Attributes: a system that has a direct impact on the logical execution of a program
  It defines the system in an abstract manner
  It deals with What does the system do
  Instruction set, number of bits used for data representation, I/O mechanisms, addressing techniques
  e.g. Is there a multiply instruction?
Notes: The first step in understanding computer architecture is learning its language.
The words in a computer’s language are called instructions. The computer’s vocabulary is called the instruction set.
All programs running on a computer use the same instruction set.
Even complex software applications, such as word processing and spreadsheet applications, are eventually compiled into a series of simple instructions such as add, subtract, and jump.
Computer instructions indicate both the operation to perform and the operands to use. The operands may come from memory, from registers, or from the instruction itself.

## Slide 4: Architecture & Organisation
Organization is how features are implemented
  Deals with structural relationship
  Attributes: hardware details transparent to the programmer
  Is the way in which a system must structure and It is operational units and the interconnections between them that achieve the architectural specifications
  It is the realization of the abstract model
  It deals with How to implement the system
  Control signals, interfaces between the computer and peripherals, memory technology
  e.g. Is there a hardware multiply unit or is it done by repeated addition?

## Slide 5: Architecture & Organisation
A systematic approach of deriving the solution of any problem
Manufacturers produce family of computer models
  Same architecture, different organisation
  Different models = different price and performance
Computer architecture is about "what" a computer system does, while computer organization is about "how" it does it. Architecture defines the capabilities and features, while organization determines how those features are implemented in hardware.

## Slide 6: Architecture & Organisation
All Intel x86 family share the same basic architecture
Similarly ARM Cortex-M, R and A families have the same respective ARMv7-M, R and A architectures
Notes: X86
The world's predominant hardware platform for laptops, desktops and servers.
The x86 line was developed by Intel and includes the Core, Xeon, Pentium, Atom and original 8086 family (hence the "86"). With an even greater market share than x86
ARM is the hardware platform for mobile devices and appliances
ARM cortex
ARM Cortex-M architecture highly efficient, low cost and energy-efficient processor and it has been used in millions of customer devices.
Application of cortex-M4 mainly lies in the areas where we need intense digital signal processing or we want to do math related operating in floating point format.

## Slide 7: Architecture & Organisation
Family concept allows code compatibility
  At least backwards
  Because same architecture, but organisation differs between different versions
  Customer’s software investment protected
Notes: A prominent example of both these phenomena is the IBM System/370 architecture.
This architecture was first introduced in 1970 and included a number of models.
Customers with modest requirements could buy a cheaper, slower model and, if demand increases, later upgrade to a more expensive, faster model without abandoning software that has already been developed.
Over the years, IBM has introduced many new models with improved technology to replace older models, offering the customer greater speed, lower cost, or both.
These newer models retained the same architecture to protect the customer’s software investment.

## Slide 8: Outline
Organisation and architecture
Structure and function
Computer evolution and performance
Cloud Computing
Performance Issues
  History of computers
  X86, PowerPC and ARM evolution

## Slide 9: Structure & Function
A computer is a complex system
  A hierarchical system is a set of interrelated subsystems
  At each level, look into the components and their interrelationships
Notes: 9
A computer is complex; contemporary computers contain millions of elementary electronic components.
How, then, can one clearly describe them? The key is to recognize the hierarchical nature of most complex systems
A hierarchical system is a set of interrelated subsystems; each subsystem may, in turn, contain lower-level subsystems, until we reach the lowest level of elementary subsystem

## Slide 10: Structure & Function
Structure is the way in which components relate to each other
Function is the operation of the individual component as part of the structure
Notes: 10

## Slide 11: Structure & Function
In terms of description, we have two choices:
Starting at the bottom and building up to a complete description
Beginning with a top view and decomposing the system into its subparts
Bottom-up
Top-down
Notes: 11

## Slide 12: Structure & Function
Clearer to describe computer system using top-down approach
  start with major components (their structure & function)
  proceed to the lower layer

## Slide 13: Function
Data processing
Data storage
Data movement
Control
All computer functions are:
Notes: Both the structure and functioning of a computer are, in essence, simple.
In general terms, there are only four basic functions that a computer can perform

## Slide 14: Function
Data processing
Data storage
Data movement
Control
Data may take a wide variety of forms and different processing requirements
Even though the computer process the data on the fly, the computer must temporarily store at least those pieces of data
Short term vs long term data storage
Input-output (I/O) Peripheral
Manages the computer resources
All computer functions are:
Notes: Data processing: Data may take a wide variety of forms, and the range of processing requirements is broad. However, we shall see that there are only a few fundamental methods or types of data processing.
Data storage: Even if the computer is processing data on the fly (i.e., data come in and get processed, and the results go out immediately), the computer must temporarily store at least those pieces of data that are being worked on at any given moment. Thus, there is at least a short-term data storage function. Equally important, the computer performs a long-term data storage function. Files of data are stored on the computer for subsequent retrieval and update.
Data movement: The computer’s operating environment consists of devices that serve as either sources or destinations of data. When data are received from or delivered to a device that is directly connected to the computer, the process is known as input–output (I/O), and the device is referred to as a peripheral. When data are moved over longer distances, to or from a remote device, the process is known as data communications.
Control: Within the computer, a control unit manages the computer’s resources and orchestrates the performance of its functional parts in response to instructions.

## Slide 15: Functional View

## Slide 16: Operations (a) Data movement
Notes: Every computer has an input and output device that makes the computer move data between itself and outside the world
The input devices are meant for entering the data into the computer. It is the data that we need to process. The output devices are where the computer displays the produced result or the output data.

## Slide 17: Operations (b) Storage
Notes: Once the processing has been done there must be some means to store the final and intermediate results.
Even though it seems that we enter the data into the computer, it processes that data and immediately produces the result.
But still, the computer needs to store those pieces of data that are being worked on at the current moment.

## Slide 18: Operation (c) Processing from/to storage
Notes: If we talk of the computer, basically we consider it for performing computation. So, there must be a unit in the computer that would perform computation.
For performing computation this unit must be capable of processing data.
It is the data processing unit that processes the data.
It must also be able to process data in a wide variety of forms.

## Slide 19: Operation (d) Processing from storage to I/O
Notes: The computers are also capable of moving data over a longer distance i.e., to or from a remote device.
We refer to this moving of data between the remote devices as data communication.

## Slide 20: Control a unit that would control and synchronize the function of these units
Notes: However, controlling of these three units is regulated by the individual who provides the instruction to the computer. In response to these instructions the control unit manages the resources of the computer and controls the performance of the functional units.

## Slide 21: Function
Data processing
Data storage
Data movement
Control
Which is the most important?
?

## Slide 22: Function
Data processing
Data storage
Data movement
Control
Which is the “busiest”?
?

## Slide 23: Function
Data processing
Data storage
Data movement
Control
So, which is the most important? 

## Slide 24: Structure
Internal structure of a computer:
4 main components
  Central processing unit (or processor)
    controls the operation and performs data processing
  Main memory
    stores data
  I/O
    moves data between the computer and its external environment
  System interconnection
    mechanism for communication among CPU, main memory and I/O
Notes: We begin with a traditional computer with a single processor that employs a microprogrammed control unit, then examine a typical multicore structure.

## Slide 25: Structure Top Level
Computer
Peripherals
Communication
lines
Main
Memory
Input
Output
Systems
Interconnection
Central
Processing
Unit
Computer
Notes: Central processing unit (CPU): Controls the operation of the computer and performs its data processing functions; often simply referred to as processor.
Main memory: Stores data.
I/O: Moves data between the computer and its external environment.
System interconnection: Some mechanism that provides for communication among CPU, main memory, and I/O.

## Slide 26: Structure Top Level (Hardware)
Source: https://www.123rf.com/photo_9645973_black-stylish-desktop-pc-isolated-on-white-background.html
Source: https://www.legitreviews.com/gigabyte-ga-965p-ds3-motherboard-review_418

## Slide 27: Structure Top Level (Hardware)
Source: https://kb.stonegroup.co.uk/ index.php?CategoryID=7#f543
Asus H110M-A

## Slide 28: Structure Top Level (Hardware)

## Slide 29: Structure Top Level
Computer
Peripherals
Communication
lines
Main
Memory
Input
Output
Systems
Interconnection
Central
Processing
Unit
Computer

## Slide 30: Structure The CPU
Computer
Memory
System
Bus
Arithmetic
and
Logic Unit
Control
Unit
Internal CPU
Interconnection
Registers
CPU
I/O
CPU

## Slide 31: Structure The Control Unit
CPU
Registers
Internal
Bus
Control
Memory
Control Unit
Registers and
Decoders
Sequencing
Logic
Control Unit
ALU
Control
Unit

## Slide 32: Structure
Computer
  Central processing unit (or CPU or processor)
  Main memory
  I/O
  System interconnection
Central processing unit
  Arithmetic and logic unit (or ALU)
  Registers
  Control unit
  Internal CPU interconnection
What can you notice?
TOP
DOWN

## Slide 33: Multicore Computer Structure
Contemporary computers generally have multiple processors
When these processors all reside on a single chip, the term multicore computer is used, and each processing unit (consisting of a control unit, ALU, registers, and perhaps cache) is called a core

## Slide 34: Multicore Computer Structure
Terminology
  Central processing unit (CPU)
    Fetches and executes instructions
    Consists of an ALU, a control unit, and registers
    Referred to as a processor in a system with a single processing unit
  Core
    An individual processing unit on a processor chip
    May be equivalent in functionality to a CPU on a single-CPU system
    Specialized processing units are also referred to as cores

## Slide 35: Multicore Computer Structure
Terminology
  Processor
    Containing one or more cores
    Interprets and executes instructions
    Referred to as a multicore processor if it contains multiple cores

## Slide 36: Multicore Computer Structure

## Slide 37
Image source: https://www.flickr.com/photos/29143375@N05/4582236533
Reflection…
From the lecture today,
I learnt…
Link on eLearn / Chat