## Slide 1
Stallings, Computer Organization & Architecture (9th Ed.), Chapter 9
Hamacher, Vranesic, & Zaky, Computer Organization (5th Ed.), Appendix E
Attendance

## Slide 2: Computer Organisation
Topic 2
Number Systems
Stallings, Computer Organization & Architecture (9th Ed.), Chapter 9
Hamacher, Vranesic, & Zaky, Computer Organization (5th Ed.), Appendix E

## Slide 3
What do you see?
1234

## Slide 4: Outline
Decimal systems
Binary systems
Converting between binary and decimal
Converting between hexadecimal and binary
Character Codes
Notes: LO
Understand the basic concepts and terminology of positional number systems
Explain the techniques for converting

## Slide 5: Introduction
One of the characteristics of digital systems:
  To represent and manipulate discrete elements of information (10 decimal digits, 26 alphabet letters, 64 squares of chessboard)
Notes: The number system is a way to represent or express numbers.
You have heard of various types of number systems such as the whole numbers and the real numbers.
But in the context of computers, we define other types of number systems.

## Slide 6: Number systems
Decimal Number System (Base-10) – commonly used
Binary Number System (Base-2) – two values ONLY
Octal Number System (Base-8) – commonly used in computer programming context
Hexadecimal Number System (Base-16) – commonly used in CS and programming
Other Number Systems
  Base-12 (Duodecimal)
  Base-60 (Sexagesimal)
  Base-64 (encoding data for transmission)
Notes: Besides decimal number, binary (base 2), octal (base 8) and Hexadecimal (base 16) are commonly used in the digital electronics system

## Slide 7: Types of number system
Binary
Octal
Decimal
Hexadecimal
Base or radix (r)
The value representing the number system
The range of digit representing each base
0 to r-1
Base/radix = 2
The range of digits = 0 to (2-1) = 0 to 1
Base/radix = 8
The range of digits = 0 to (8-1) = 0 to 7
Base/radix = 10
The range of digits = 0 to (10-1) = 0 to 9
Base/radix = 16
The range of digits = 0 to (16-1) = 0 to 15

## Slide 8: Quick Activity #0
Identify the radix for the following numbers:
283
54
215
2C
1011

## Slide 9: Positional Number Systems
In a positional number system, each number represented by a string of digits in which each digit position i has an associated weight ri, where r is the radix, or base, of the number system.
The value of any digit ai is an integer in the range 0 ≤ i < r.
The dot between a0 and a-1 is called the radix point.
As an example of another positional system, consider the system with base 7.

## Slide 10: Introduction
Bits in a computer system are grouped together into cells
An eight-bit memory cell in main memory
0
1
1
0
1
0
1
0
1
1
0
1
1
0
0
1
0
0
0
0
0
0
0
0
1
7
1
0
2
0
2
0
N
O
V
E
M
B
E
R
Notes: INFO
Computer memories are designed with a most remarkable property
Each storage location can contain either a high-voltage signal or a low-voltage signal ( never anything in between)
The storage location is like being pregnant. Either you are or you are not. There is no halfway 

## Slide 11: Decimal
The decimal number system is also known as the base 10 system
It is referred to as base 10 because it has 10 different symbols
The based 10 system is also said to have radix of 10
We use decimal systems with decimal digits
  0, 1, 2, 3, 4, 5, 6, 7, 8, 9

## Slide 12: The Decimal System
Consider what the number 83 means?
Eight tens plus three
83 = (8 x 10) + 3
What about 4728?
Four thousands, seven hundreds, two tens, plus eight
4728 = (4 x 1000) + (7 x 100) + (2 x 10) + 8

## Slide 13: The Decimal System
A decimal system is a base or radix of 10
  The number multiply by 10 to the power of the digit’s position (place value)
83 = (8 x 101) + (3 x 100)
4728 = (4 x 103) + (7 x 102) + (2 x 101) + (8 x 100)
0
1
0
1
2
3
20
21
22
23
2n
2-n
2-3
2-2
2-1
.
x
x
x
x
÷
÷
÷

## Slide 14: The Decimal System
The same principles apply to fraction but with negative powers of 10s
0.256 = (2 x 10-1) + (5 x 10-2) + (6 x 10-3)
-1
-2
-3
2
1
0
-1
-2
-3
442.256 = (4 x 102) + (4 x 101) + (2 x 100) + (2 x 10-1)
+ (5 x 10-2) + (6 x 10-3)
0
Leftmost digit = Most Significant bit (MSB)
Rightmost digit = Least Significant bit (LSB)

## Slide 15: The Decimal System
Positional interpretation of a decimal number
Leftmost digit = Most Significant Bit (MSB)
Rightmost digit = Least Significant Bit (LSB)
Notes: shows the relationship between each digit position and the value assigned to that position. Each position is weighted 10 times the value of the position to the right and one-tenth the value of the position to the left.

## Slide 16: Quick research
How many tens are in the 509?
Notes: Five hundreds and nine
(5x102) + (0x101) + (9x100)

## Slide 17: Introduction
Discrete elements are represented by signals
  Signals have two discrete values: 0 and 1, binary values -> binary digit (bit)
Digital
Binary
Bit
signal stored in memory can have only a fixed number of value
only two values are possible
0 or 1
Notes: INFO
Computer memories are designed with a most remarkable property
In digital electronics, we only deal with 2 possible states (High and Low, ON and OFF, or Open and Closed)
Therefore, for this reason, almost all digital systems use the binary (base 2) number system as the system of its operation
Each storage location can contain either a high-voltage signal or a low-voltage signal ( never anything in between)
The storage location is like being pregnant. Either you are or you are not. There is no halfway 

## Slide 18: The Binary System
To avoid confusion, we will sometimes put a subscript on a number to indicate its base
For larger numbers, each digit in a binary number has a value depending on its position (as in decimal system)

## Slide 19: The Binary System
Binary number are strings of two (hence “bi”) symbols 0’s and 1’s, that represent numbers.
10 different digits are used to represent numbers with a base of 10
There are only two digits, 1 and 0
  Hence base 2
1
0
4
8
1310

## Slide 20: The terminology
BIT
Each digit in the binary system
NIBBLE
A group of 4 bits binary
BYTE
WORD
A group of 8 bits binary
Two bytes number

## Slide 21: The Binary System
21
102 = (1 x 21) + (0 x 20) = 210
112 = (1 x 21) + (1 x 20) = 310
1002 = (1 x 22) + (0 x 21) + (0 x 20) = 410
In general, for the binary representation of Y = 5cb2b1b0.b-1b-2b-3c6 , the value of Y is
1001.102 = (1 x 23) + (0 x 22) + (0 x 21) + (1 x 20) + (1 x2-1) + (0 x 2-2) + (2 x 2-3) = 9.75 10
1001.102 = (1 x 23) + (1 x 20) + (1 x2-1) + (2 x 2-3) = 9.75 10
20 = 1

## Slide 22
Spot the difference +
X =
Decimal
Binary

## Slide 23
What other (popular) number systems are there?
research +

## Slide 24: In a nutshell
The binary system is closely tied to Boolean logic, a mathematical system used for representing and manipulating logical values (true and false)
Binary is the natural language of digital electronics.
Data storage in computers, including hard drives and memory, is organized into binary data structures.
Overall, the binary system is fundamental to the operation of computers and digital technology, as it provides a simple and efficient way to represent and process information in a digital form.
Notes: Boolean logic forms the basis for designing digital circuits and programming logic.
Computers and other digital devices use binary signals to represent and process information.
These signals consist of variations in voltage or current, where a high voltage (often represented as 1) indicates a "true" or "on" state, and a low voltage (often represented as 0) indicates a "false" or "off" state.
Each piece of data, such as a character, number, or instruction, is encoded using a binary representation

## Slide 25: Converting From: Binary To Decimal
Multiply each binary digit by the appropriate power of 2 and add the results
Notes: It is a simple matter to convert a number from binary notation to decimal notation
All that is required is to multiply each binary digit by the appropriate power of 2 and add the results
To convert from decimal to binary, the integer and fractional parts are handled separately.

## Slide 26: Converting From: Binary To Decimal
Example:
(10101.11)2  ( )10
(a3 a2 a1 a0.a-1 a-2)2  ( )10
(a323 + a222 + a121 + a020+.a-12-1 + a-22-2)r  ( )10
1 | a4
0 | a3
1 | a2
0 | a1
1 | a0
1 | a-1
1 | a-2
4 3 2 1 0 -1-2
(1x24) + (0x23) + (1x22) + (0x21) + (1x20) + (1x2-1) + (1x2-2)
16 + 0 + 4 + 0 + 1 + 0.5+ 0.25
1
21
1
22
21.75

## Slide 27: Converting From: Decimal To Binary (Integer)
(13)10  ( )2
To convert decimal to any other base ‘r’, divide integer part by r and multiply fractional part by r
13
2
6
1
2
3
0
2
1
1
2
0
1
Dividend
Remainder
Divisor (r)
Most Significant bit
Less Significant bit
?
1101
13
2
6
12
1
6
2
3
6
0
3
2
1
2
1
1
2
0
0
1

## Slide 28: Converting From: Decimal To Binary (Integer)
(11)10  ( )2
11
2
5
1
2
2
1
2
1
0
2
0
1
11
2
5
10
1
5
2
2
4
1
2
2
1
2
0
1
2
0
0
1
1011

## Slide 29: Converting From Decimal To Binary
Decimal integer N to binary with N1 as quotient and R0 remainder
,
,

## Slide 30: Converting From Decimal To Binary (Fractions)
(25.625)10  ( )2
?
11001
25
Integer
0.625
Fraction
25
2
12
1
2
6
0
2
3
0
2
1
1
2
1
0
11001.101
0.625 x 2 = 1.25
0.25 x 2 = 0.50
0.50 x 2 = 1.00
0.00 x 2 = 0.00
101
Step 1
Step 2
÷
x

## Slide 31: Converting From Decimal To Binary (Fractions)
Notes: A decimal fraction with a finite number of digits may require a binary fraction with an infinite number of digits. In such cases, the conversion algorithm is usually halted after a prespecified number of steps, depending on the desired accuracy.

## Slide 32: Converting From Decimal To Binary (Fractions)
,

## Slide 33: The Hexadecimal Notation
Binary notation is cumbersome
Converting to decimal – tedious
Notes: Cumbersome = slow or complicated and therefore inefficient.
Because of the inherent binary nature of digital computer components, all forms of data within computers are represented by various binary codes.
However, no matter how convenient the binary system is for computers, it is exceedingly burdensome for human beings.
Consequently, most computer professionals who must spend time working with the actual raw data in the computer prefer a more compact notation.
One possibility is the decimal notation. This is certainly more compact than binary notation, but it is awkward because of the tediousness of converting between base 2 and base 10.

## Slide 34: The Hexadecimal Notation
In hexadecimal number system, we have 16 different digits
Each one of them can be represented by equivalent 4-bit binary number
Better option is hexadecimal – 16 digits 0…9, A, B, C, D, E, F
r=16
Notes: Instead, a notation known as hexadecimal has been adopted.
the decimal system uses ten digits: 0 to 9. Of course, you can count beyond 9. To do so you simply use more than one digit. So, to get past 9 you change the value to 0 and add a 1 to the left. That gives you the number 10.
The base-2 system has just two values: 0 and 1. To represent a number greater than 1 you again use more than one digit. To get to the number 2 you change the number to 0 and stick a 1 in front of it. So, in base-2 the number 2 is written as 10.
Base-16 uses 16 values: the numbers 0 to 9 and the letters A to F. Up to the number 9 the decimal and hexadecimal systems are identical: a base-10 number 9 is also a 9 in base-16. We don’t have a single number for ten, which is why base-16 uses the letters A to F. The letter A is 10, B is 11 etc.

## Slide 35: The Hexadecimal Notation
r = 16
0 will be the first digit
Plus 15 other digits
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111
(10)
(11)
(12)
(13)
(14)
(15)
Notes: Hexadecimal is a numbering system with base 16. It can be used to represent large numbers with fewer digits.
In this system there are 16 symbols or possible digit values from 0 to 9, followed by six alphabetic characters -- A, B, C, D, E and F. These characters are used to represent decimal values from 10 to 15 in single bits.

## Slide 36: The need for hexadecimal numbers
In computing systems, the binary string equivalents of large decimal numbers can become quite long.
When 16- or 32-bit numbers are involved, it becomes difficult to read and write them without producing errors.
These problems can be overcome by arranging the binary numbers into groups of four bits, i.e., by using the hexadecimal numbering system.
The format of hex numbers is more compact than binary numbers because they can represent large binary numbers with fewer digits.
As a result, they are easier to understand than long binary strings of 1s and 0s.

## Slide 37: Hexadecimal to Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111
(10)
(11)
(12)
(13)
(14)
(15)
1. (259A)16 ( )2
2 = 0010
5 = 0101
9 = 1001
A = 1010
0010 0101 1001 1010
2. (CAFE.3D)16 ( )2
C = 1100
A = 1010
F = 1111
E = 1110
3 = 0011
D = 1101
1100 1010 1111 1110 0011 1101

## Slide 38: Binary to Hexadecimal
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111
(10)
(11)
(12)
(13)
(14)
(15)
(10001001.11)2 ( )16
1. Group the integer into 4 bits
10001001.11
2. For the digit with insufficient bit, you will add 00 to complete the group of 4 bits
10001001.11
00
(89.C)16

## Slide 39: Binary to Hexadecimal
The binary number is divided into groups of four digits = nibble
=
1101
1110
0001
D
E
1
DE116
1101111000012
Notes: Binary digits are grouped into sets of four bits, called a nibble. Each possible combination of four binary digits is given a symbol, as follows

## Slide 40: Binary to Hexadecimal
The binary number is divided into groups of four digits
10110001101011.11110010 =
2C6B.F216
2
00
C
6
B
.
F
2

## Slide 41: Decimal to Hexadecimal
(479)10

( ? )16
Step 1
479 ÷ 16 = 29.9375 =
29
0.9375 x16 = 15
29 R 15
29 ÷ 16 = 1.8125 =
1
0.8125 x16 = 13
1 R 13
1 ÷ 16 = 0.0625 =
0
0.0625 x16 = 1
0 R 1

## Slide 42: Decimal to Hexadecimal
(479)10

( )16
Step 1
29 R 15
1 R 13
0 R 1
1
13
15
1
D
F
1DF

## Slide 44: In a nutshell
Hexadecimal notation is not only used for representing integers but also used as a concise notation for representing any sequence of binary digits, whether they represent text, numbers, or some other type of data
The reasons for using hexadecimal notation:
  It is more compact than binary notation.
  In most computers, binary data occupy some multiple of 4 bits, and hence some multiple of a single hexadecimal digit.
  It is extremely easy to convert between binary and hexadecimal notation.

## Slide 45
Convert the above octal number to decimal.
5678

## Slide 46
Convert the above octal number to decimal.
What numbers did you add to get the answer?
5678

## Slide 47: Conversion summary
Binary2
Octal8
Hexadecimal16
Decimal10
(d x rn) + (d x rn) ………
(÷) with R
Arrange R B-U
Decimal10
Binary2
Octal8
Hexadecimal16

## Slide 48: Conversion summary
Binary2
Hexadecimal16
Grouping of a Nibble
Octal8
Grouping of 3-bits digit
Decimal10
(d x rn) + (d x rn) ………

## Slide 49
Convert the above hexadecimal number to octal.
A9816

## Slide 50: Character Codes : BCD
Decimal digits
  Binary Coded Decimal (BCD) code
Decimal digit | BCD code
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
Notes: Binary Coded Decimal, or BCD, is another process for converting decimal numbers into their binary equivalents.
It is a form of binary encoding where each digit in a decimal number is represented in the form of bits.
This encoding can be done in either 4-bit or 8-bit (usually 4-bit is preferred).
It is a fast and efficient system that converts the decimal numbers into binary numbers as compared to the existing binary system.
These are generally used in digital displays where is the manipulation of data is quite a task.
Thus BCD plays an important role here because the manipulation is done treating each digit as a separate single sub-circuit.

## Slide 51: Character Codes : ASCII
ASCII stands for American Standard Code for Information Interchange
7-bit ASCII codes (American Standards Committee on Information Interchange)
ASCII codes represent text in computers, communications equipment, and other devices that use text
This code is basically used for identifying characters and numerals in a keyboard.
ASCII is a character encoding method that uses a 7-bit code to represent 128 characters, which include letters, numbers, and special characters.

## Slide 52: ASCII Code

## Slide 53
Character Codes : EBCDIC
An 8-bit character encoding used mainly on IBM mainframe and IBM midrange computer operating systems
EBCDIC has 256 characters and is used to represent a wide variety of characters, such as letters, numbers, special characters, and control characters.

## Slide 54
Character Codes : EBCDIC

## Slide 55
Image source: https://www.flickr.com/photos/29143375@N05/4582236533
Reflection…
Watch video on Format Wars: ASCII vs EBCDIC.
Who won/lost and why?
Link on eLearn / Chat