## Slide 1: Computer Organisation
Topic 3
Computer Arithmetic
Stallings, Computer Organization & Architecture (9th Ed.), Chap. 10

## Slide 2: Outline
  Sign-magnitude
  Twos complement
  Conversion between lengths
  Addition & Subtraction
  Multiplication
  Division
Floating-point Arithmetic
Integer Arithmetic
Integer Representation
Arithmetic & Logic Unit

## Slide 3: Learning objectives
Understand the distinction between the way in which numbers are represented (the binary format) and the algorithms used for the basic arithmetic operations.
Explain twos complement representation.
Present an overview of the techniques for doing basic arithmetic operations in twos complement notation.
Understand the use of significand, base, and exponent in the representation of floating-point numbers.

## Slide 4: Arithmetic & Logic Unit
A vital component of the CPU responsible for executing arithmetic and logical instructions
A fundamental part of a computer's processing capabilities
Other elements of the computer system (CU, registers, memory) mainly to bring data into the ALU for it to process and then to take the results back out
Does the calculations
Everything else in the computer is there to service this unit
Image source: https://www.wannapik.com/vectors/10124
Notes: 4
Computer arithmetic is commonly performed on two very different types of numbers: integer and floating point.
In both cases, the representation chosen is a crucial design issue and is treated first, followed by a discussion of arithmetic operations
All of the other elements of the computer system—control unit, registers, memory, I/O—are there mainly to bring data into the ALU for it to process
and then to take the results back out. We have, in a sense, reached the core or essence of a computer when we consider the ALU.
An ALU and indeed, all electronic components in the computer, are based on the use of simple digital logic devices that can store binary digits and perform simple Boolean logic operations

## Slide 5: Arithmetic & Logic Unit
Handles integers
May handle floating point (real) numbers
Notes: 5

## Slide 6: ALU Inputs and Outputs
Image source: https://www.wannapik.com/vectors/10124
Notes: 6
how the ALU is interconnected with the rest of the processor. Operands for arithmetic and logic operations are presented to the ALU in registers, and the results of an operation are stored in registers. These registers are temporary storage locations within the processor that are connected by signal paths to the ALU
The ALU may also set flags as the result of an operation. For example, an overflow flag is set to 1 if the result of a computation exceeds the length of the register into which it is to be stored
The flag values are also stored in registers within the processor. The processor provides signals that control the operation of the ALU and the movement of the data into and out of the ALU

## Slide 7: Outline
  Sign-magnitude
  Twos complement
  Conversion between lengths
  Addition & Subtraction
  Multiplication
  Division
Floating-point Arithmetic
Integer Arithmetic
Integer Representation
Arithmetic & Logic Unit

## Slide 8: Integer Representation
The way in which whole numbers (integers) are represented in a digital computer/binary system
Only have 0 & 1 to represent everything
Positive numbers stored in binary
  e.g. 41=00101001
Binary digit or a ????
Bit
Notes: 8
In the binary number system,1 arbitrary numbers can be represented with just the digits zero and one, the minus sign (for negative numbers), and the period, or radix
point (for numbers with a fractional component).

## Slide 9
Data Representation
Magnitude
Complement
Unsigned
Signed
1’s complement
2’s complement
(+ve)
(+ve) & (-ve)
(+ve) & (-ve)
(+ve) & (-ve)
In all representation, (+) number is represented in the same way

## Slide 10: Integer Representation
In the binary system, number system can be represented with just the digits 0 and 1
No minus sign, no period, no radix point
Two ways:
Sign-Magnitude
Two’s complement
Notes: 10
For purposes of computer storage and processing, however, we do not have the benefit of special symbols for the minus sign and radix point. Only binary digits (0 and
1) may be used to represent numbers. If we are limited to nonnegative integers, the representation is straightforward.

## Slide 11
Data Representation
Magnitude
Complement
Unsigned
Signed
1’s complement
2’s complement
(+ve)
(+ve) & (-ve)
(+ve) & (-ve)
(+ve) & (-ve)
In all representation, (+) number is represented in the same way
Notes: Sign-Magnitude Representation
There are several alternative conventions used to represent negative as well as positive integers, all of which involve treating the most significant (leftmost) bit in the word as a sign bit.
If the sign bit is 0, the number is positive; if the sign bit is 1, the number is negative.
The simplest form of representation that employs a sign bit is the sign-magnitude representation.

## Slide 12: Unsigned magnitude
Represents positive integers
Position | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
Bit Pattern | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
Weight | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
10011101 = unsigned representation of 157

## Slide 13: Unsigned magnitude
Only accept positive numbers
In computer programming, the unsigned integers property open for application in most numeric data types:
  Short
  Long
  Int
  Char

## Slide 14: Advantages and disadvantages of unsigned magnitude
Advantages
  One representation of zero
  Simple addition
Disadvantages
  Negative numbers cannot be represented
  The need of different notation to represent negative numbers

## Slide 15: Is a representation of negative numbers possible?
Unfortunately,
You cannot just stick a negative sign in front of a binary number (it does not work like that)
There are three methods used to represent negative numbers:
Signed magnitude notation
1s complement notation
2s complement notation

## Slide 16: Signed-magnitude
Human use the signed-magnitude system.
We add + or – to the front of a number to indicate its sign
We can do this in binary too! By adding a sign bit in front of our numbers.

## Slide 17: Signed-Magnitude
Use one-bit to represent the sign of the integer
Left most bit (Most Significant Bit, MSB) is sign bit
0 means positive
1 means negative
  +18 = 00010010
  -18 = 10010010
Notes: 17
In signed magnitude representation, a number is represented by two parts: a sign bit and a magnitude (or absolute value) part. The sign bit indicates whether the number is positive or negative, with 0 typically representing positive and 1 representing negative. The magnitude part represents the absolute value of the number.

## Slide 18: Signed-Magnitude
+6 =
-6 =
0
1
Magnitude
Sign bit
Most significant bit (MSB)
110
110
0 = (+)
1 = (-)
Notes: 18

## Slide 19: Signed-Magnitude
+13 =
-13 =
1101
1101
1
0
0 = (+)
1 = (-)
Notes: 19

## Slide 20: Signed-magnitude
Suppose 10011101 is a signed magnitude representation.
The sign bit is 1, then the number represented is negative
Position | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
Bit Pattern | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
Weight |  |  |  | 16 | 8 | 4 |  | 1
The magnitude is 0011101 with a value of 24+ 23 22+ 20 = 29
Then, the number represented by 10011101 is -29.

## Slide 21: Signed-Magnitude Range
The range of signed magnitude representation depends on the number of bits used for both the sign bit and the magnitude part
Sign Bit part: 1 bit (1 for negative, 0 for positive)
Magnitude Part: (n-1) bits (assuming 1 bit is used for the sign)
The range of values that can be represented in signed magnitude representation with n bits is typically:
Range of signed magnitude = - (2n-1 -1) to +(2n-1 -1)
n = number of bit
Notes: 21

## Slide 22: Signed-Magnitude Range
Example:
n = 4
- (2n-1 -1) to +(2n-1 -1)
n = number of bit
- (24-1 -1) to +(24-1 -1)
- (23 -1) to +(23 -1)
- (23 -1) to +(23 -1)
- (8 -1) to +(8 -1)
- (7) to + (7)
Answer:
The signed magnitude for 4 bit are between:
Notes: 22

## Slide 23: Drawbacks of sign-magnitude
Addition and subtraction require a consideration of both the signs of the numbers and their relative magnitudes to carry out the required operation.
They are two representations of 0
To test if a number is 0 or not, the CPU will need to see whether it is 00000000 or 10000000.
Therefore, having 2 representation of 0 is inconvenient.
00000000 = +010
10000000 = -010

## Slide 24: Quick Activity #1
3710 has 00100101 is signed magnitude notation. Find the signed magnitude of -3710.
Using the signed magnitude notation find the 8-bit binary representation of the decimal value 2410 and -2410.
Find the signed magnitude of –63 using 8-bit binary sequence?

## Slide 25
1010010

## Slide 26
Data Representation
Magnitude
Complement
Unsigned
Signed
1’s complement
2’s complement
(+ve)
(+ve) & (-ve)
(+ve) & (-ve)
(+ve) & (-ve)
In all representation, (+) number is represented in the same way

## Slide 27: 1s complement
In a different representation, 1s complement, we negate numbers by complementing each bit of the number.
We keep the sign bits; 0 for positive and 1 for negative
The sign bit is complemented along with the rest of the bits

## Slide 28: 1’s complement
Negative numbers are represented by taking the bitwise complement (inverting all the bits) of the positive binary representation of the number
(1010)2 = (0101)2

## Slide 29: 2’s complement
2's complement is a binary representation method used in computers to represent signed integers (both positive and negative numbers).
It is the most common method for representing signed integers
2’s complement requires 2 rules:
Find 1’s complement for the integer
Add 1 to the 1’s complement
Rule 1
Rule 2

## Slide 30: 2’s complement
Example:
(10111010)2
Step 1: Find 1’s complement for the integer
Step 2: Add 1 to the 1’s complement
Step 1
01000101
Step 2
01000101
1
+
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 0 carry forward 1
0
1
1
1
0
0
0
1
0

## Slide 31: 2’s complement (Alt)
+3 = 00000011
+2 = 00000010
+1 = 00000001
+0 = 00000000
-1 = 11111111
-2 = 11111110
-3 = 11111101
Most significant bit (MSB) is sign bit
One representation of zero
= 1’s complement
1
2
Add 1 to LSB
3
(Left)
(Right)

## Slide 32: 2’s complement
+3 = 00000011
+2 = 00000010
+1 = 00000001
+0 = 00000000
-1 = 11111111
-2 = 11111110
-3 = 11111101
+3 = 00000011
1
1’s complement
11111100
2
Add 1 to LSB
11111101
3

## Slide 33: 2’s complement (Alt)
+3 = 00000011
+2 = 00000010
+1 = 00000001
+0 = 00000000
-1 = 11111111
-2 = 11111110
-3 = 11111101
Identify the LSB and copy all zeros until the first 1
Copy the first 1
1
2
Complement all the remaining bits (after 1)
3

## Slide 34: 2’s complement
+3 = 00000011
+2 = 00000010
+1 = 00000001
+0 = 00000000
-1 = 11111111
-2 = 11111110
-3 = 11111101
+3 = 00000011
1
11111101
2

## Slide 35: Quick Activity #2
010012
010112
001112
000012
Notes: 101112
101012
110012
111112

## Slide 36: Characteristics of 2’s Complement Representation
- (2n-1) to +(2n-1 -1)
n = number of bit

## Slide 37: Advantages of 2’s complement
It eliminates the need for two representations of zero, resulting in a unique representation.
Arithmetic operations like addition, subtraction, and multiplication are simplified, and there are no issues with end-around carries.
The representation is symmetric, meaning the range of positive and negative values is evenly distributed around zero.
It's widely supported and used in modern computer systems due to its efficiency in arithmetic operations and other benefits.

## Slide 38: Advantages of 2’s complement
Subtraction can be easily performed
Multiplication is just a repeated addition
Division is just a repeated subtraction
2s complement is widely used in ALU

## Slide 39: Converting Between 2’s Complement Binary To Decimal
An eight-position 2’s complement value box
Position | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
Weight | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Bit Pattern |  |  |  |  |  |  |  | 
Notes: The most negative 2s complement range is -(2n-1)
-(28-1)
-(27)
-(128)
2. If any of the bits other than the sign bit is one, it adds a positive amount to the number
3. A negative number must have a 1 at its leftmost position and a positive number must have a 0 in that position.
4. Thus, the largest positive number is a 0 followed by all 1s, which equals 2n - 1 - 1.

## Slide 40: Converting Between 2’s Complement Binary To Decimal
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
-128
+2
+1
10000011 =-125
Example:
Convert binary 10000011 to decimal
1
0
0
0
0
0
1
1
10000011 = -128 + 2 + 1
10000011 = -128 + 3
Notes: The most negative 2s complement range is -(2n-1)
-(28-1)
-(27)
-(128)
2. If any of the bits other than the sign bit is one, it adds a positive amount to the number
3. A negative number must have a 1 at its leftmost position and a positive number must have a 0 in that position.
4. Thus, the largest positive number is a 0 followed by all 1s, which equals 2n - 1 - 1.

## Slide 41: Converting Between 2’s Complement Decimal To Binary
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
+8
120 = 01111000
Example:
Convert decimal 120 to binary
0
1
1
1
1
0
0
0
64 + 32 + 16 + 8= 01111000
+16
+32
+64
Notes: The most negative 2s complement range is -(2n-1)
-(28-1)
-(27)
-(128)
2. If any of the bits other than the sign bit is one, it adds a positive amount to the number
3. A negative number must have a 1 at its leftmost position and a positive number must have a 0 in that position.
4. Thus, the largest positive number is a 0 followed by all 1s, which equals 2n - 1 - 1.

## Slide 42: Converting Between 2’s Complement Decimal To Binary
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
-128
+8
-120 = 10001000
Example:
Convert decimal -120 to binary
1
0
0
0
1
0
0
0
-128 + 8 = 10001000
Notes: The most negative 2s complement range is -(2n-1)
-(28-1)
-(27)
-(128)
2. If any of the bits other than the sign bit is one, it adds a positive amount to the number
3. A negative number must have a 1 at its leftmost position and a positive number must have a 0 in that position.
4. Thus, the largest positive number is a 0 followed by all 1s, which equals 2n - 1 - 1.

## Slide 43: In-class activity
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
10100101
66
-80
Convert the following:
01101101

## Slide 44: Negation
In signed-magnitude representation, the rule for forming the negation of an integer is simple: invert the sign bit.
In twos complement notation, the negation of an integer can be formed with the following rules:
  Find 1’s complement to the integer
  Add 1 to 1’s complement integer

## Slide 46: Quick Activity #3
Represent these numbers in 8-bit 2’s complement
+ 44
+ 89
+ 106
- 18
- 74
- 86
- 99
- 110
- 120
- 128

## Slide 47: 2’s complement operations
Addition
Subtraction
Multiplication
Division

## Slide 48: Addition in 2’s in complement

## Slide 49: Addition and Subtraction
Addition proceeds as if the two numbers were unsigned integers
If the result of the operation is positive, we get a positive number in 2’s complement form, which is the same as in unsigned integer form
If the result of the operation is negative, we get a negative number in 2’s complement form
In some instances, there is a carry bit beyond the end of the word (indicated by shading), which is ignored
On any addition, the result may be larger than can be held in the word size being used = OVERFLOW
When overflow occurs, the ALU must signal this fact so that no attempt is made to use the result

## Slide 50: Overflow rule
If two numbers are added, and they are both positive or both negative, then overflow occurs if and only if the result has the opposite sign.
(+) + (+) = (-)
(-) + (-) = (+)
Sign bit
0 +
1-

## Slide 51: Rules of Binary Arithmetic
Binary Addition
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 0 Sum of 0 with a carry of 1
Binary Subtraction
0 – 0 = 0
1 – 0 = 1
1 – 1 = 0
0 = 1 = 1 (Borrow 1)
Binary Multiplication
0 × 0 = 0
0 × 1 = 0
1 × 0 = 0
1 × 1 = 1

## Slide 52: Addition (Example 1)
Add two 4-bits 2’s complement of 4 and 3
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
4 |  |  |  |  | 0 | 1 | 0 | 0
3 |  |  |  |  | 0 | 0 | 1 | 1
Step 1 – Convert 4 and 3 to binary
Step 2 – Perform binary addition
4 |  |  |  |  | 0 | 1 | 0 | 0
3 |  |  |  |  | 0 | 0 | 1 | 1
 |  |  |  |  | 0 | 1 | 1 | 1
Answer: 4 + 3 = 7 = 0111

## Slide 53: Addition (Example 2)
Add two 5-bit 2’s complement of 13 and -6
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
13 |  |  |  | 0 | 1 | 1 | 0 | 1
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
+6 |  |  |  | 0 | 0 | 1 | 1 | 0
-6 |  |  |  | 1 | 1 | 0 | 1 | 0
13 |  |  | 0 | 1 | 1 | 0 | 1
-6 |  |  | 1 | 1 | 0 | 1 | 0
 |  | 1 | 0 | 0 | 1 | 1 | 1
Step 2 – Perform binary addition
Step 1 – Convert 13 and -6 to binary
In 2s complement
Answer: 13 + (-6) = 7 = 00111
Notes: To subtract B from A, take the 2s complement of B and add it to A.

## Slide 54: Addition (Example 3)
Add two 5-bit 2’s complement of -15 and 9
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
9 |  |  |  | 0 | 1 | 0 | 0 | 1
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
+15 |  |  |  | 0 | 1 | 1 | 1 | 1
-15 |  |  |  | 1 | 0 | 0 | 0 | 1
15 |  |  | 1 | 0 | 0 | 0 | 1
-6 |  |  | 0 | 1 | 0 | 0 | 1
 |  |  | 1 | 1 | 0 | 1 | 0
Step 2 – Perform binary addition
Step 1 – Convert -15 and 9 to binary
In 2s complement
Answer: -15 + 9= -6 = 11010
Notes: To subtract B from A, take the 2s complement of B and add it to A.

## Slide 55: Addition (Example 4)
Add two 8-bit 2’s complement of -39 and 92
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
92 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
+39 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
-39 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1
-39 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1
92 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
Step 2 – Perform binary addition
Step 1 – Convert -39 and 92 to binary
In 2s complement
Answer: -39 + 92= 53= 00110101
Notes: To subtract B from A, take the 2s complement of B and add it to A.

## Slide 56: Addition (Example 5)
Add two 5-bit 2’s complement of -8 and -4
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
+8 |  |  | 0 | 1 | 0 | 0 | 0
-8 |  |  | 1 | 1 | 0 | 0 | 0
+4 |  |  | 0 | 0 | 1 | 0 | 0
-4 |  |  | 1 | 1 | 1 | 0 | 0
-8 |  |  | 1 | 1 | 0 | 0 | 0
-4 |  |  | 1 | 1 | 1 | 0 | 0
 |  | 1 | 1 | 0 | 1 | 0 | 0
Step 2 – Perform binary addition
Step 1 – Convert -8 and -4 to binary
Answer: -8 + (-4)= -12 = 10100
Notes: To subtract B from A, take the 2s complement of B and add it to A.

## Slide 57: Addition (Example 4)
Add two 8-bit 2’s complement of 104 + 45
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
104 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0
45 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1
104 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0
45 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1
 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
Step 2 – Perform binary addition
Step 1 – Convert 104 and 45 to binary
Answer: 104 + 45 = 149 = 10010101
Overflow example
Notes: 104 + 45 = 149 = 10010101

## Slide 58: How do we handle overflow?
Since we added two positive numbers and got a negative result, overflow has indeed occurred. Therefore, this answer is not correct for 8-bit representation.
So, the correct answer cannot be represented within an 8-bit signed integer and would require a larger bit width (like 9 bits or more) to hold the value accurately.

## Slide 59: Quick Activity #4
Assume numbers are represented in 8-bit twos-complement representation. Show the calculation of the following:
-19 + (-7)
44 + 45
-75 + 59
127 + 1
-1+1
-103 + (-69)

## Slide 61: 2’s complement operations
Addition
Subtraction
Multiplication
Division

## Slide 62: Subtraction in 2’s complement
To subtract one number (subtrahend) [S] from another (minuend) [M], take the 2s complement (negation) of the subtrahend and add them to the minuend
[M] + 2s [S]
Step 1: Find 2s complement of subtrahend [S]
Step 2: Perform the addition
Step 3: If the carry bit is generated and the result is positive, and in its true form
If carry bit is not produced, then the result is negative and in its 2s complement form
0 +
1-
Notes: If the carry bit is generated and the result is positive, and in its true form
If carry bit is not produced, then the result is negative and in its 2s complement form

## Slide 63: Subtraction (Example 1)
Subtract two 4-bit 2’s complement of 2 and -7
S | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
7 |  |  |  |  | 0 | 1 | 1 | 1
-7 |  |  |  |  | 1 | 0 | 0 | 1
M | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
2 |  |  |  |  | 0 | 0 | 1 | 0
+2 |  |  |  |  | 0 | 0 | 1 | 0
+7 |  |  |  |  | 0 | 1 | 1 | 1
 |  |  |  |  | 1 | 0 | 0 | 1
Step 2 – Perform binary addition
Step 1 – Convert 2 and -7 to binary
Answer: 2 –(-7) = 2 + 7 = 9
M = 2
S = -7
Overflow example
Notes: If the carry bit is generated and the result is positive, and in its true form
If the carry bit is generated and the result is negative, we ignore the carry bit
If carry bit is not produced, then the result is negative and in its 2s complement form

## Slide 64: Subtraction (Example 2)
Subtract two 4-bit 2’s complement of 5 and -2
S | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
2 |  |  |  |  | 0 | 0 | 1 | 0
M | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
5 |  |  |  |  | 0 | 1 | 0 | 1
5 |  |  |  |  | 0 | 1 | 0 | 1
2 |  |  |  |  | 0 | 0 | 1 | 0
 |  |  |  |  | 0 | 1 | 1 | 1
Step 2 – Perform binary addition
Step 1 – Convert 5 and -2 to binary
Answer: 5 – (-2) = 5 + 2 = 7 = 0111
M = 5
S = -2
Notes: If the carry bit is generated and the result is positive, and in its true form
If the carry bit is generated and the result is negative, we ignore the carry bit
If carry bit is not produced, then the result is negative and in its 2s complement form

## Slide 65: Subtraction (Example 3)
Subtract two 4-bit 2’s complement of 5 and -3
M | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
+5 |  |  |  |  | 0 | 1 | 0 | 1
+5 |  |  |  |  | 0 | 1 | 0 | 1
+3 |  |  |  |  | 0 | 0 | 1 | 1
 |  |  |  | 1 | 0 | 0 | 0 | 0
Step 2 – Perform binary addition
Step 1 – Convert -5 and -2 to binary
Answer: 5 –(-3) = 5 +3 = 8
S | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
+3 |  |  |  |  | 0 | 0 | 1 | 1
M =5
S =-3
Overflow example
Notes: If the carry bit is generated and the result is positive, and in its true form
If the carry bit is generated and the result is negative, we ignore the carry bit
If carry bit is not produced, then the result is negative and in its 2s complement form

## Slide 66: Subtraction (Example 4)
Subtract two 4-bit 2’s complement of 5 and 2
M | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
+5 |  |  |  |  | 0 | 1 | 0 | 1
+2 |  |  |  |  | 0 | 0 | 1 | 0
-2 |  |  |  |  | 1 | 1 | 1 | 0
5 |  |  |  |  | 0 | 1 | 0 | 1
-2 |  |  |  |  | 1 | 1 | 1 | 0
 |  |  |  | 1 | 0 | 0 | 1 | 1
Step 2 – Perform binary addition
Step 1 – Convert 5 and 2 to binary
Answer: 5 – (+2) = 5 – 2 = 3 = 0011
M =5
S =2
Notes: If the carry bit is generated and the result is positive, and in its true form
If the carry bit is generated and the result is negative, we ignore the carry bit
If carry bit is not produced, then the result is negative and in its 2s complement form

## Slide 67: Subtraction (Example 5)
Subtract two 4-bit 2’s complement of 7and 7
M | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
7 |  |  |  |  | 0 | 1 | 1 | 1
-7 |  |  |  |  | 1 | 0 | 0 | 1
7 |  |  |  |  | 0 | 1 | 1 | 1
-7 |  |  |  |  | 1 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0 | 0
Step 2 – Perform binary addition
Step 1 – Convert 7 to binary
Answer: 7– 7= 0 = 10000
M =7
S =7
Notes: To subtract B from A, take the 2s complement of B and add it to A.

## Slide 68: Subtraction (Example 6)
Subtract two 4-bit 2’s complement of 7and -7
M | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
7 |  |  |  |  | 0 | 1 | 1 | 1
7 |  |  |  |  | 0 | 1 | 1 | 1
7 |  |  |  |  | 0 | 1 | 1 | 1
 |  |  |  |  | 1 | 1 | 1 | 0
Step 2 – Perform binary addition
Step 1 – Convert 7 to binary
Answer: 7–(-7) = 14 = 1110
M =7
S =-7
Overflow example
Notes: If the carry bit is generated and the result is positive, and in its true form
If the carry bit is generated and the result is negative, we ignore the carry bit
If carry bit is not produced, then the result is negative and in its 2s complement form

## Slide 69: Subtraction (Example 3)
Subtract two 4-bit 2’s complement of 5 and -6
M | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
+5 |  |  |  |  | 0 | 1 | 0 | 1
+5 |  |  |  |  | 0 | 1 | 0 | 1
+6 |  |  |  |  | 0 | 1 | 1 | 0
 |  |  |  |  | 1 | 0 | 1 | 1
Step 2 – Perform binary addition
Step 1 – Convert -5 and -2 to binary
Answer: 5 – (-6) = 5 + 6 = 11
S | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
+6 |  |  |  |  | 0 | 1 | 1 | 0
M =5
S =-6
Overflow example
Notes: If the carry bit is generated and the result is positive, and in its true form
If the carry bit is generated and the result is negative, we ignore the carry bit
If carry bit is not produced, then the result is negative and in its 2s complement form

## Slide 70: Quick Activity #5
Assume numbers are represented in 8-bit twos-complement representation. Show the calculation of the following:
5 – 3
7 – 4
−6−2
12−(−5)
−7−(−8)
45−18
−50−25

## Slide 71: Hardware for Addition and Subtraction
Notes: 71
Figure suggests the data paths and hardware elements needed to accomplish addition and subtraction.
The central element is a binary adder, which is presented two numbers for addition and produces a sum and an overflow indication.
The binary adder treats the two numbers as unsigned integers.
For addition, the two numbers are presented to the adder from two registers, designated in this case as A and B registers.
The result may be stored in one of these registers or in a third.
The overflow indication is stored in a 1-bit overflow flag (0 = no overflow; 1 = overflow). For subtraction, the subtrahend (B register) is passed through a twos complementer so that its twos complement is presented to the adder.
Control signals are needed to control whether or not the complementer is used, depending on whether the operation is addition or subtraction.

## Slide 72
+---------------------------------+
| Arithmetic Unit |
+----------------+----------------+
|
+------------+------------+
| |
+---+---+ +---+---+
| | | |
| Adder | |Subtractor|
| | | |
+---+---+ +---+---+
| |
+---+---+ +---+---+
| | | |
| Input | | Input |
| Ports | | Ports |
| | | |
+---+---+ +---+---+
| |
+---+------------------------+---+
| Multiplexer |
+----------------+---------------+
|
+---+---+
| Output |
| Port |
+---+---+
The control signals for the multiplexer determine whether the arithmetic unit performs addition or subtraction.
The output of the selected operation is then passed to the output port.
This basic hardware setup can be expanded and optimized for more complex arithmetic operations and can be part of a larger CPU or digital processing system.
Notes: Arithmetic Unit: This is the main processing unit responsible for performing addition and subtraction operations. It consists of both an adder and a subtractor.
Adder: The adder is a component that performs addition operations. It takes input from input ports and produces the sum as output.
Subtractor: The subtractor is a component that performs subtraction operations. It also takes input from input ports and produces the difference as output.
Input Ports: These are the interfaces through which the numbers to be added or subtracted are provided to the arithmetic unit.
Multiplexer: The multiplexer is used to select whether to perform addition or subtraction based on the control signals. It directs the input to either the adder or the subtractor.
Output Port: This is the interface through which the result of the addition or subtraction operation is outputted.