## Slide 1: Computer Organisation
Topic 3
Computer Arithmetic
(Part 2)
Stallings, Computer Organization & Architecture (9th Ed.), Chap. 10

## Slide 2: Outline
  Sign-magnitude
  Twos complement
  Conversion between lengths
  Addition & Subtraction
  Multiplication
  Division
Floating-point Arithmetic
Integer Arithmetic
Integer Representation
Arithmetic & Logic Unit

## Slide 3: 2’s complement operations
Addition
Subtraction
Multiplication
Division
Add-shift method (unsigned integer)
Booth’s algorithm (-ve numbers)

## Slide 4: Multiplication
Compared with addition and subtraction, multiplication is a complex operation, whether performed in hardware or software.
A wide variety of algorithms have been used in various computers.
Work out partial product for each digit
Take care with place value (column)
Add partial products
Notes: 4

## Slide 5: Multiplication of unsigned integer

## Slide 6: 11 x 13
11 = multiplicand
13 = multiplier
 |  |  |  |  | 1 | 0 | 1 | 1
 |  |  |  | X | 1 | 1 | 0 | 1
 |  |  |  |  | 1 | 0 | 1 | 1
 |  |  |  | 0 | 0 | 0 | 0 | x
 |  |  | 1 | 0 | 1 | 1 | x | x
 |  | 1 | 0 | 1 | 1 | x | x | x
 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1
11
13
Note:
  if multiplier bit is 1 copy multiplicand (place value) otherwise zero
  Need double length result
Partial products
Addition operation
Pencil and paper approach
Notes: Multiplication involves the generation of partial products, one for each digit in the multiplier. These partial products are then summed to produce the final product.
The partial products are easily defined. When the multiplier bit is 0, the partial product is 0. When the multiplier is 1, the partial product is the multiplicand
The total product is produced by summing the partial products. For this operation, each successive partial product is shifted one position to the left relative to the preceding partial product.

## Slide 7: Multiplication
How can this be more efficient?
  Perform running addition on partial products
          Do not have to wait until the end
          Fewer registers are needed
This eliminates the need for storage of all the partial products
Notes: Compared with the pencil-and-paper approach, there are several things we can do to make computerized multiplication more efficient.

## Slide 8: Multiplication
How can this be more efficient?
  2. Save time on generation of partial products
      For each 1 on multiplier requires an add and a shift operation
      For each 0 on multiplier, only a shift is required

## Slide 9: Multiplication block diagram
Note:
M remains the same
C, A & Q involved in shifting
C
M: (11)10
Q: (13)10
A: (additional register)
C: Carry bit
Notes: This multiplication block diagram illustrate the concept of multiplication in the ALU
Multiplicand and multiplier are loaded into 2 registers (Q and M )
Next, the third register, A is needed to and initially set to 0
Then, we have a 1-bit register, C that was also initialized to 0 to hold the potential carry bit (for any addition process)
How did operations work?
CU read the Q register one bit at a time and if Q0 =1, the multiplicand is added to the A register and result will be stored to A. (C is required for carry bit or overflow cases)
Then, all of the bits of the C, A and Q registers are shifted to the right ONE bit so that C bit goes into A(n-1) , A0 goes into Q(n-1) and Q0 is lost
Then, no addition is performed, just the shift

## Slide 10: Unsigned Binary Multiplication
M: Multiplicand = (11)10
Q: Multiplier = (13)10
A: (additional register)
C: Carry bit
Note:
M remains the same
C, A & Q involved in shifting
    For each 1 on multiplier requires an add and a shift operation
    For each 0 on multiplier, only a shift is required

## Slide 11: Flowchart for Unsigned Binary Multiplication

## Slide 12: 11 x 13
11 = multiplicand
13 = multiplier
 |  |  |  |  | 1 | 0 | 1 | 1
 |  |  |  | X | 1 | 1 | 0 | 1
 |  |  |  |  | 1 | 0 | 1 | 1
 |  |  |  | 0 | 0 | 0 | 0 | x
 |  |  | 1 | 0 | 1 | 1 | x | x
 |  | 1 | 0 | 1 | 1 | x | x | x
 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1
11
13
Pencil and paper approach
Notes: Multiplication involves the generation of partial products, one for each digit in the multiplier. These partial products are then summed to produce the final product.
The partial products are easily defined. When the multiplier bit is 0, the partial product is 0. When the multiplier is 1, the partial product is the multiplicand
The total product is produced by summing the partial products. For this operation, each successive partial product is shifted one position to the left relative to the preceding partial product.

## Slide 13
(11)10 x (13)10
(11)10 = (1011)2
(13)10 = (1101)2
1
1
0
1
1
0
1
1
1
1
0
1
0
0
0
0
1
1
0
1
1
1
0
1
1
0
0
0
1
1
1
1
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 0 carry forward 1
1
1
1

## Slide 14
(13)10 x (9)10
(13)10 = (1101)2
(9)10 = (1001)2
1
0
1
1
1
0
0
1
1
0
1
1
0
0
0
0
0
0
0
0
1
0
1
1
0
1
1
1
1
0
1
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 0 carry forward 1
1
0
= (117)10

## Slide 15: Multiplication using Add-shift method
11 x 13
11 = M (multiplicand)
13 = Q (multiplier)
143 = AQ

## Slide 16
Hardware Structure for add-shift multiplication
n-bit Adder
Shift and Add control logic
C
Multiplicand (M)
Mn-1
Mn-2
M1
M0
Qn-1
Qn-2
Q1
Q0
Register (A)
An-1
An-2
A1
A0
Multiplier (Q)
Shift Right
1 bit register
Notes: 4 different registers – multiplicand(M), multiplier(Q), register (A) and Register (C)
Out of these 4 registers, (M), (A) and (Q) are n bit register – depending on the number of bit
C register is the 1-bit register to handle the overflow
N-bit adder to perform the n-bit addition process
Control logic = to perform the shift and addition process --- send signal to adder as well as registers

## Slide 17
Initialize C, A to 0
Fill the (M) and (Q) with the binary value
  Count = bit value
N cycle:
  Check the Q0 value
    If 1 = Add value in (A) and (M)
      Shift RIGHT (C), (A) and (Q)
      Count – 1
    If 0 = Shift RIGHT (C), (A) and (Q)
      Count -1
Final cycle = count = 0

## Slide 18
C | A | Q | Operation | Cycle
0 | 0000 | 1011 | Initial | 
0 0 | 1101 0110 | 1011 1101 | Add (A+M) Shift right | 1st
1 0 | 0110 1001 | 1101 1110 | Add (A+M) Shift right | 2nd
0 | 0100 | 1111 | Shift right | 3rd
1 0 | 0001 1000 | 1111 1111 | Add (A+M) Shift right | 4th
13 (Multiplicand) = 1101
11 (QMultiplier) = 1011
13 x 11
Expected results:
(143)10
(10001111)2
Shift count = bit count
Add count = 1 count in Q

## Slide 19
C | A | Q | Operation | Cycle
13 (Multiplicand) = 1101 (remain unchanged)
11 (QMultiplier) = 1011
13 x 11
Expected results:
(143)10
(10001111)2
0
0000
n=4
1 0 1 1
initialization
-
Q0
Q1
Q2
Q3
A+M
0000
1101
1101
+
1101
Shift  C, A & Q
0
1
1
0
1
1
0
1
1
0
1
1
1st cycle
A+M
0110
1101
10011
+
0011
0
1
0
1001
1110
Shift  C, A & Q
1
1
0
1
2nd cycle
Shift  C, A & Q
0
0100
1111
3rd cycle
0
A+M
0100
1101
10001
+
0001
1
1000
1111
1111
Shift  C, A & Q
4th cycle
0

## Slide 20
C | A | Q | Operation | Cycle
0 | 0000 | 1110 | Initial | 
0 | 0000 | 0111 | Shift C, A &Q | 1st
0 0 | 1100 0110 | 0111 0011 | Add A+M Shift C, A &Q | 2nd
1 0 | 0010 1001 | 0011 0001 | Add A+M Shift C, A &Q | 3rd
1 0 | 0101 1010 | 0001 1000 | Add A+M Shift C, A &Q | 4th
12 (Multiplicand) = 1100
14 (QMultiplier) = 1110
12 x 14
Expected results:
(168)10
(10101000)2

## Slide 21: Quick activity #7
Multiply the following values using add-shift multiplication method:
10 x 10
9 x 12

## Slide 23: How we handle multiplication of two negative numbers?

## Slide 24: Multiplying Negative Numbers (2s Complement)
1011
1101
1011
0000
1011
1011
10001111
x
Multiplicand (-5 decimal)
Multiplier (-3 decimal)
Partial products
Product (?? decimal)
Notes: 24

## Slide 25: Multiplying Negative Numbers (2s Complement)
1011
1101
1011
0000
1011
1011
10001111
x
Multiplicand (-5 decimal)
Multiplier (-3 decimal)
Partial products
Product (-113 decimal)
Notes: 25
If the multiplier is negative, straightforward multiplication also will not work.
The reason is that the bits of the multiplier no longer correspond to the shifts or multiplications that must take place.

## Slide 26: Multiplying Negative Numbers (2s Complement)
Solution 1
  Convert to positive if required
  Multiply as above
  If signs were different, negate answer
    Implementers prefer techniques that do not require this final transformation step

## Slide 27: Multiplying Negative Numbers (2s Complement)
Solution 2
  Booth’s algorithm
  Multiplies two signed binary numbers in 2s complement notation
  Invented by Andrew Donald Booth in 1950s
Notes: One of the most common of these is Booth’s algorithm. This algorithm also has the benefit of speeding up the multiplication process, relative to a more straightforward approach.

## Slide 28: Booth’s Algorithm conditions
Q3Q2Q1Q0Q-1
Q0 | Q-1 | Operation
0 | 0 | Shift right A, Q, Q-1
1 | 1 | 
0 | 1 | Add (A+M) Shift right A, Q, Q-1
1 | 0 | Subtract (A-M) Shift right A, Q, Q-1
Notes: Q-1 =1-bit register placed logically to the right of the least significant bit (Q0) of the Q register
control logic scans the bits of the multiplier one at a time.
Now, as each bit is examined, the bit to its right is also examined.
If the two bits are the same (1–1 or 0–0), then all of the bits of the A, Q, and Q-1 registers are shifted to the right 1 bit.
If the two bits differ, then the multiplicand is added to or subtracted from the A register, depending on whether the two bits are 0–1 or 1–0.
Following the addition or subtraction, the right shift occurs.
In either case, the right shift is such that the leftmost bit of A, namely An - 1, not only is shifted into An - 2, but also remains in An - 1.
This is required to preserve the sign of the number in A and Q.
It is known as an arithmetic shift, because it preserves the sign bit.

## Slide 29: Booth’s algorithm
7 (Multiplicand) = 0111(remain unchanged)
3 (QMultiplier) = 0011
7 x 3
Expected results:
(21)10
(10101)2

## Slide 30: Booth’s algorithm
7 (Multiplicand) = 0111(remain unchanged)
3 (QMultiplier) = 0011
7 x 3
Expected results:
(21)10
(10101)2
1
0
0
1
0
0
1
1
Notes:   Rule 1: Find 2’s complement of the subtracted number
  Rule 2: Perform the addition

## Slide 31: Booth’s Algorithm
Example 2

## Slide 32
A | Q | Q-1 | M | Operation | Cycle
7 (Multiplicand) = 0111
-6 (QMultiplier) = 1010
0000
1010
0
0111
0000
0101
0
0111
Shift
Shift
1100
1010
0111
1
A+M
0011
1010
0001
1
0111
1101
0
0111
Shift
1010
1101
1101
0
0111
0110
1
0111
Shift
Initialize
A-M = A+2sM
1001
0101
0
0111
A-M = A+2sM
1st cycle
2nd cycle
3rd cycle
4th cycle
2s M = 1001

## Slide 33: Booth’s Algorithm
Example 3

## Slide 34: Case 1: 4 x 4
M = 4 = 0100
Q = 4 = 0100
2s M = 1100
A | Q | Q-1 | Operation | Cycle
0000
0100
0
Init.
Shift
_000
0010
0
0
Shift
0000
0001
0
A-M
0000
1100
1100
1100
0001
0
Shift
_110
0000
1
1
A+M
1110
0100
10010
0010
0000
1
Shift
0001
0000
0

## Slide 35: Case 1: 4 x -4
M = 4 = 0100
Q = -4 = 1100
2s M = 1100
A | Q | Q-1 | Operation | Cycle
2s Q = 0100
0000
1100
0
Init.
Shift
0000
0110
0
Shift
0000
0011
0
A-M
0000
1100
1100
1100
0011
0
Shift
1110
0001
1
Shift
1111
0000
1

## Slide 36: Case 1: -4 x 4
M = -4 = 1100
Q = 4 = 0100
2s M = 0100
A | Q | Q-1 | Operation | Cycle
0000
0100
0
Init.
Shift
0000
0010
0
Shift
0000
0001
0
A-M
0000
0100
0100
0100
0001
0
Shift
0010
0000
1
A+M
1110
0000
1
0010
1100
1110
Shift
1111
0000
0

## Slide 37: Case 1: -4 x -4
M = -4 = 1100
Q = -4 = 1100
2s M = 0100
A | Q | Q-1 | Operation | Cycle
0000
1100
0
Init.
Shift
0000
0110
0
Shift
0000
0011
0
A-M
0000
0100
0100
0100
0011
0
Shift
0010
0001
1
Shift
0001
0000
1
2s Q = 0100

## Slide 38: Advantages of Booth’s Algorithm
Performed signed multiplications
Performs better of –ve numbers are involved
Reduced number of operations

## Slide 39: Quick activity #8
Use the Booth algorithm to multiply 23 (multiplicand) by 29 (multiplier), where each number is represented using 6 bits
Use the Booth algorithm to multiply 10 (multiplicand) by -10 (multiplier), where each number is represented using 5 bits
Use the Booth algorithm to multiply -6 (multiplicand) by -5 (multiplier), where each number is represented using 4 bits
Use the Booth algorithm to multiply -7 (multiplicand) by 5(multiplier), where each number is represented using 4 bits
Given x = 0100 and y = 1100 in twos complement notation (i.e., x = 4, y = -4), compute the product p = x * y with Booth’s algorithm

## Slide 40: 2’s complement operations
Addition
Subtraction
Multiplication
Division

## Slide 41: Division
Division is somewhat more complex than multiplication but is based on the same general principles.
As before, the basis for the algorithm is the paper-and-pencil approach, and the operation involves repetitive shifting and addition or subtraction.
Notes: 41

## Slide 42: Long method division
Dividend (M) = 128
Divisor (Q) = 8
1
2
8
1<8
0
0
-
1
2
12>8
8
4
8
48>8
4
8
0
8
1
6
Quotient (or Answer) = 16
Remainder = 0

## Slide 43: Long method division
1<110
0
0
-
1
0
1
Quotient (or Answer) = 111
Remainder = 0
Dividend (M) = 101010
Divisor (Q) = 110
(42)10
(6)10
0
1
0
1
1
0
1
0
1
0
10<110
0
0
0
1
1
101<110
0
0
0
1
1
0
1010>110
1
0
1
1
0
0
1
1
1001>110
1
0
1
1
0
1
1
0
110<110
1
0
1
1
-
-
-
-
-

## Slide 44: Flowchart for Unsigned Binary Division
Initial A register, Load M&Q register
Shift left (A & Q)
A – M operation
Look at A condition:
  A<0 = T = Q0 gets a 1 bit
  A<0 = F = Q0 gets a 0 bit and restores M the previous value

## Slide 45: Division in 2s complement
7 ÷ 3 = 2 with 1 remainder (Q ÷ M)
Q = 0111
M = 0011
0111
0011
011
0001
0000
0001
(3)
(7)

## Slide 46
2sM =1101
(-3)
(-1)
(0)
(-1)

## Slide 47: Q (Dividend) = 7 = 0111 M (Divisor) = 3 = 0011 2sM = 1101
A | Q | Operation
0000
0111
Shift (L)
111_
0000
Init.
A-M
0000
1101
1101
1101
(-3)
Restore A, Q0 = 0
0000
1110
0
Shift (L)
110_
0001
A-M
0001
1101
1110
1110
(-1)
Restore A, Q0 = 0
0001
0
1100
Shift (L)
100_
0011
A-M
0011
1101
10000
0000
(0)
Subtract, Q0 = 1
0000
0
1001
Shift (L)
001_
0001
A-M
0001
1101
1110
1110
(-1)
Restore A, Q0 = 0
0001
0
0010

## Slide 50: Quick activity #9
Execute the division for the following binary numbers using the long division method and restoring 2s complement division. You must show the full complete process side by side.
4 ÷ 2
9 ÷ 3
10 ÷ 4
11 ÷ 3

## Slide 51: Outline
  Sign-magnitude
  Twos complement
  Conversion between lengths
  Addition & Subtraction
  Multiplication
  Division
Floating-point Arithmetic
Integer Arithmetic
Integer Representation
Arithmetic & Logic Unit

## Slide 52: Introduction
Numbers
Fixed point
Floating point
Integers 1,21, 456
Fractions
0.5, 0.25, 0.123
1.52
15.2
456.123
Notes: With a fixed-point notation (e.g., twos complement) it is possible to represent a range of positive and negative integers centered on or near 0. By assuming a fixed binary or radix point, this format allows the representation of numbers with a fractional component as well.

## Slide 53: Real numbers
Numbers with fractions
Could be done in pure binary
E.g.:
1001.1010 = 23 + 20 + 2-1 + 2-3 = 9.625
Notes: Very often when we deal with numbers, we not only deal with integers, but we also deals with real numbers, numbers that are in fractions….
Very often this could be done in pure binary…
So binary numbers can also be used to represent real numbers as well….

## Slide 54: Real numbers
With a fixed-point notation (e.g., twos complement) it is possible to represent a range of positive and negative integers centered on or near 0.
HOWEVER, this approach has limitations
Cannot represent a very LARGE numbers nor very SMALL fractions.
For decimals, we overcome this limitation by using scientific notation
976,000,000,000,000
9.76 x 1014
0.0000000000000976
9.76 x 10-14
Notes: What we have done, in effect, is dynamically to slide the decimal point to a convenient location and use the exponent of 10 to keep track of that decimal point.
This allows a range of very large and very small numbers to be represented with only a few digits.

## Slide 55: Real numbers
Where is the binary or radix point?
Fixed?
  Very limited
Moving?
  How do we show where it is?
Notes: If you fixed the radix point, you will have limitation in representing the fractions for either larger or smallest number
If you want it to move, how do you show where the fraction starts?

## Slide 56: Floating-point representation
What about binary numbers?
± S x B ±E
Sign: plus, or minus
Significand S
Exponent E
Notes: So, one way to store floating point is to have it in a particular format

## Slide 57: Signs for Floating Point
Significand is stored in 2s complement
Exponent is in biased notation
  e.g. Bias of 127 means (2k-1 – 1), k is number of bits
    8-bit exponent field
      Pure value range 0-255
      Range -127 to +128
    Subtract 127 to get the correct value
Notes: 57

## Slide 58
Sign of number
(0=+ | 1=-)
Exponent value is stored in the next 8 bits
Biased Exponent
Significand
8 bits
23 bits
32 bits
Floating-point representation
fractional part of a number
1.6328125 x 220
=
1.101001 x 210100
Notes: 1.6328125 x 220
How do we express this numbers in binary?

## Slide 59: Floating-point representation
1.6328125 x 220
=
1.101001 x 210100
1. The original value of exponent = 20
2. To get the exponent value in binary = original exponent + bias exponent
20 + 127 = 147  10010011
3. The biased exponent value is = 10010011
Biased Exponent
Significand
S
10010011
Notes: The original value of exponent is 20, and one of the way to represent the floating point numbers is using the biased exponent
In this case, the biased exponent is kept in 8 bit and the biased exponent for 8-bit is 127
How do we get the exponent value in binary?

## Slide 60: Floating-point representation
1.6328125 x 220
=
1.1010001 x 210100
How do we get the significand value?
2. Convert the fractional portion to binary
0.6328125 to binary = 101001
3. Therefore, the significand is 101001 + remaining 0 to fulfil 23 bits
Biased Exponent
Significand
S
10010011
10100010000000000000000
Notes: Now, how do we get the significand value?
In this case, the biased exponent is kept in 8 bit and the biased exponent for 8-bit is 127
How do we get the exponent value in binary?

## Slide 61: Floating-point representation
1.6328125 x 220
=
1.1010001 x 210100
How do we identify the sign value?
0 = (+) and 1 (-)
Biased Exponent
Significand
S
10010011
10100010000000000000000
0
Notes: Now, how do we get the significand value?
In this case, the biased exponent is kept in 8 bit and the biased exponent for 8-bit is 127
How do we get the exponent value in binary?

## Slide 62
Floating-point representation
Tip: 20 + 127 = 147
Tip: -20 + 127 = 107
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1 | 1

## Slide 63: Normalization
Floating point numbers are usually normalized
  i.e. exponent is adjusted so that leading bit (MSB) of significand is 1
Since it is always 1 there is no need to store it
  23 bits can store 24-bit number
c.f. Scientific notation where numbers are normalized to give a single digit before the decimal point
  e.g. 3.123 x 103
Notes: 63
To simplify operations on floating-point numbers, it is typically required that they be normalized.

## Slide 64
Expressible Numbers
(32 bits)
(1 sign bit, 8 bit exponent, 23-bit significand)
1.0… x
1.111… =
The smallest (+) number can be represented
The biggest (+) number can be represented
2,147,483,647
-2,147,483,647

## Slide 65: IEEE 754
The most important floating-point representation is defined in IEEE Standard 754, adopted in 1985 and revised in 2008.
This standard was developed to facilitate the portability of programs from one processor to another and to encourage the development of sophisticated, numerically oriented programs.
The standard has been widely adopted and is used on virtually all contemporary processors and arithmetic coprocessors. IEEE 754-2008 covers both binary and decimal floating-point representations.
Standard for floating point storage
32- 64- and 128-bit standards
8, 11 and 15-bit exponent respectively
Extended formats (both significand and exponent) for intermediate results
Notes: 65

## Slide 66: IEEE 754

## Slide 68: Floating Point Arithmetic
FP operation may cause
  Exponent overflow
    Positive exponent exceed maximum possible value
    May be +  or - 
  Exponent underflow
    Negative exponent less than the minimum possible
    Number too small, may be reported as 0
  Significand underflow
    When aligning, digits flow off the right end of significand
  Significand overflow
    Carry out of most significant bit
    E.g. when adding 2 significand of same sign

## Slide 69: FP Arithmetic Addition/Subtraction
More complicated than multiplication/division
  Need for alignment
4 phases
Check for zeros
Align significands (adjusting exponents)
Add or subtract significands
Normalize result
Notes: 69

## Slide 70: FP Addition & Subtraction Flowchart

## Slide 71
FP Multiplication Flowchart

## Slide 72
FP Division Flowchart

## Slide 73: Quick Activity #10
The following numbers use the IEEE 32-bit floating-point format. What is the equivalent decimal value?
0 10000000 10100000000000000000000
1 10000010 00100000000000000000000

## Slide 74: Quick Activity #11
Express the following numbers in IEEE 32-bit floating-point format
-5
-6
384
1/16

## Slide 75: Quick Activity #11
Express the following numbers in IEEE 32-bit floating-point format
-5
Biased Exponent
Significand
S
01111111
1
01000000000000000000000
Determine the sign bit
Convert the integer to binary value
Determine the exponent
  For 32-bit floating point, we will be using 8-bit biased exponent
Determine the significand
Notes: Significand is the fractional portion, the component of a floating-point representation
How do we determine the significand for 5?
Normalize the binary fraction, in this case of 5, the binary value is 101, and normalization is when the MSB is set to 1 so that we do not have to store the value
In this case of 5, the MSB is 1 and no changes is made to the binary value
Therefore, the significand for 5 is 01.

## Slide 76
Image source: https://www.flickr.com/photos/29143375@N05/4582236533
Reflection…
From the lecture today, I learnt……
Link on eLearn / Chat